## Slide 1: Shared Memory Architecture and Cache Coherency

## Slide 2: Outline
Overview of shared memory architectures
Interconnects
Memory hierarchy
Cache coherence
  Update vs. invalidate
  Snoopy vs. directory
Reading:
  Chpt2 of Kumar’s book

## Slide 3: Shared Address Space Machines
All processors share a single global address space
Single address space facilitates a simple programming model
C
P
C
P
C
I
M
Caches
Processors P
Interconnect
Memory M M
P
C
P
C
I
M M
C Caches
P Processors
Interconnect
M Memory
(a) UMA
(b) NUMA

## Slide 4: Example: Shared Address Space Machines
name | Maximum # of procs | Processor name | Processor clock rate
Compaq ProLiant 5000 | 4 | Pentiium Pro | 200MHz
Digital AlphaServer 8400 | 12 | Alpha 21164 | 440MHz
HP 9000 K460 | 4 | PA-8000 | 180MHz
IBM RS/6000 R40 | 8 | PowerPC 640 | 112MHz
SGI Power Challenge | 36 | MIPS R10000 | 195MHz
Sun Enterprise 6000 | 30 | UltraSPARC 1 | 167MHz
name | Maximum # of procs | Processor name | Processor clock rate
Cray T3E | 2048 | Alpha 21164 | 450MHz
HP/Convex Exemplar | 64 | PA-8000 | 180MHz
Sequent NUMA-Q | 32 | Pentium Pro | 200MHz
SGI Origin2000 | 128 | MIPS R10000 | 195MHz
Sun Enterprise 10000 | 64 | UltraSPARC 1 | 250MHz
(a) Characteristics of single-bus multiprocessor for sale in 1997
(b) Characteristics of network-connected Multiprocessor for sale in 1997

## Slide 5: Shared Address Space Machines
Important aspects are:
  Memory organization
  Interconnect
  Cache coherence mechanism
These aspects determine:
  Performance: programming techniques
  Scalability
  Cost

## Slide 6: Shared Memory Interconnects
Bus interconnect
  A collection of parallel communication wires together with some hardware that controls acess to the bus
  Communication wires are shared by the devices that are connected to it
  As the number of devices connected to the bus increases, contention for use of the bus increases, and performance decreases

## Slide 7: Shared Memory Interconnects
Switched interconnect
  Uses switches to control the routing of data among the connected devices
  Crossbar
    Allows simultaneous communication among different devices
    Faster than buses
    But the cost of the switches and links is relatively high
    Figure (a) a 4*4 crossbar
    Figure (b) configuration of internal switches
    Figure (c ) simultaneous memory accesses by the processors

## Slide 8: Memory Organization
Single memory shared among processors causes sequentialization of accesses
Memory interleaving
  Non-overlapping regions of address space mapped to banks
  Banks service read/write requests independently

## Slide 9: Memory Organization
00
01
00
01
00000
00001
00010
00011
00000
00001
00010
00011
10
11
10
11
Low Order Interleaving
High Order Interleaving

## Slide 10: Memory Organization
Typically, which interleaving is used? Why?
Programming issues:
  Must spread accesses across banks to avoid bank conflicts
  Involves data placement as well as code restructuring

## Slide 11: Memory Hierarchy
Most programs have a high degree of locality in their accesses
  spatial locality
  temporal locality
Memory hierarchy tries to exploit locality
on-chip
cache
datapath registers
processor control
Second level cache (SRAM)
Main memory
(DRAM)
Secondary storage (Disk)
Tertiary storage
(Disk/Tape)
Speed | 1ns | 10ns | 100ns | 10ms | 10sec
Size | KB | MB | GB | TB | PB

## Slide 12: Processor-DRAM Gap (latency)
µ Proc 60%/yr.
100
1000
CPU
Processor-Memory
“Moore’s Law”
Memory hierarchies are getting deeper
– Processors get faster more quickly than memory
7%/yr.
10
DRAM
1980
1981
1982
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
Performance Gap: (grows 50% / year)
DRAM
Performance
1
Time

## Slide 13: Handling Memory Latency
Bandwidth has improved more than latency
  23% per year vs 7% per year
Approach to address the memory latency problem
  Eliminate memory operations by saving values in small, fast memory (cache) and reusing them
    Which locality is needed?
  Take advantage of better bandwidth by getting a chunk of memory and saving it in small fast memory (cache) and using whole chunk
    Which locality is needed?
  Take advantage of better bandwidth by allowing processor to issue multiple reads to the memory system at once
    concurrency in the instruction stream, e.g. load whole array, as in vector processors; or prefetching
  Overlap computation & memory operations

## Slide 14: Little’s Law
Latency vs. Bandwidth
  Latency is physics (wire length)
    e.g., the network latency on the Earth Simulation is only about 2x times the speed of light across the machine room
  Bandwidth is cost:
    add more wires to increase bandwidth (over-simplification)
Principle (Little's Law): the relationship of a production system in steady state is:
Inventory = Throughput × Flow Time
For parallel computing, Little’s Law is about the required concurrency to be limited by bandwidth rather than latency
  Required concurrency = Bandwidth * Latency
For parallel computing, this means: Concurrency = bandwidth x latency

## Slide 15: Little’s Law
Example 1: a single processor:
If the latency is to memory is 50ns, and the bandwidth is 5 GB/s (.2ns
/ Bytes = 12.8 ns / 64-byte cache line)
What does Little’s Law tell us?
Example 2: 1000 processor system
  1 GHz clock, 100 ns memory latency, 100 words of memory in data paths between CPU and memory.
  What does Little’s Law tell us?

## Slide 16: Cache Basics
Cache is fast (expensive) memory which keeps copy of data in main memory; it is hidden from software
Cache hit
  In-cache memory access, cheap!
Cache miss
  Non-cached memory access, expensive!
Cache line length
Associativity
direct-mapped
n-way

## Slide 17: Why Multiple Levels of Cache?
On-chip vs. off-chip
  On-chip caches are faster, but limited in size
A large cache has delays
  Hardware to check longer addresses in cache takes more time
  Associativity, which gives a more general set of data in cache, also takes more time
Some examples:
  Cray T3E eliminated one cache to speed up misses
  IBM uses a level of cache as a “victim cache” which is cheaper
There are other levels of the memory hierarchy
  Register, pages (TLB, virtual memory), …
  And it isn’t always a hierarchy

## Slide 18: Cache Coherence
A significant issue with shared memory
Processors may cache the same location
If one processor writes to the location, all others must eventually see the write
X:=1
Memory

## Slide 19: Cache Coherence
P1 loads X from main memory into its cache
X:=1
Memory
P1
Load X
X:=1
Cache

## Slide 20: Cache Coherence
P1 loads X from main memory into its cache
P2 loads X from main memory into its cache
X:=1
Memory
P2
Load X
X:=1
P1
Load X
X:=1

## Slide 21: Cache Coherence
P1 stores 2 into X
We don’t have consistent values for X across the memory hierarchy
X:=1
Memory
P2
X:=1
P1
X:=2
X:=2

## Slide 22: Cache Coherence
Ensure that all processors eventually see the same value for x
Cache coherence mechanisms:
  Update vs. invalidate
  Snoopy based vs. directory based
X:=2
Memory
P2
X:=2
P1
X:=2
X:=2

## Slide 23: Approaches to Cache Coherence
Hardware
  Caches implement coherence protocols to ensure that data appears globally consistent
  Common in hardware today
Software
May or may not have help from the hardware
Must be conservative to be safe
  Assume the worst about potential memory aliases
Of increasing interest
  Concerns about cost of coherence in joules
  Scales well for microprocessor based on “tiled” designs

## Slide 24: Cache Coherence Protocols
When changing variable’s value: invalidate or update all copies
P
x
P
x
x
P
x’
P
I
P
P
x’ x’
I
Write-Invalidate
x’ Write-Update
processors
cache
memory
bus

## Slide 25: Update and Invalidate Protocols
Cost-benefit tradeoff depends upon traffic pattern
  Invalidate is worse when
• ??
  Update is worse when
• ?
Both protocols suffer from false sharing overheads
  What is false sharing?
Modern machines use invalidate protocols as the default

## Slide 26: Using Invalidate Protocols
Each copy of a data item is associated with a state
Example set of states: shared, invalid, or dirty
  Shared: multiple valid copies of the data item
    A write needs to generate an invalidate
  Dirty: only one copy exists
    A write need not generate any invalidates
  Invalidate: data copy is invalid
    A read generates a data request and updates the state

## Slide 27: Snoopy Cache Coherence
How are invalidates sent to the right processors?
  Broadcast all invalidates and read requests
  Snoopy cache listens and performs appropriate coherence operations locally
Processor Processor Processor
Tags
Snoop H/W
Cache
Tags
Snoop H/W
Cache
Tags
Snoop H/W
Cache
Dirty
Address/data
Memory
A simple snoopy bus based cache coherence system

## Slide 28: Operation of Snoopy Caches
Once a datum is tagged dirty
  All subsequent operations can be performed locally in cache
  No external traffic needed
If a data item is read by a number of processors
  Transitions to the shared state in all caches
  All subsequent read operations become local
If multiple processors read and update data
  Generate coherence requests on the bus
  Bus is BW limited: imposes a limit on updates per second

## Slide 29: The Cost of Coherence
Snoopy caches
  Each coherence op is sent to all processors
  What is the problem?
Why not send coherence requests to only those processors that need to be notified?

## Slide 30: Directory-based Cache Coherence
Directory-based: the sharing status is kept in directory
Processor
Cache
Processor
Memory
Cache
Presence
bits / State
Processor
Cache
(a)
(b)
Directory
Data
State
Presence Bits
Processor
Cache
Processor
Cache
Interconnection Network
Interconnection Network
Memory
Presence
bits / State

## Slide 31: Directory Implementations
Bit vector
  Presence bit for each cache line along with its global state
Pointer set
  Limited set of pointers (node IDs)
    Less overhead than full map
  Issue?

## Slide 32: Performance of Directory-based Schemes
Bits to store the directory may add significant overhead
  Think about scaling to many processors
    Data bits per cache block vs. presence bits per cache block
Underlying network must carry all coherence requests
Directory becomes a point of contention
  Distributed directory schemes are necessary

## Slide 33: Shared Memory Programming
In shared memory programs
  Start a single process and fork threads
  Threads carry out tasks
Dynamic threads
  Master thread waits for work, forks new threads, and when threads are done, they terminate
  Pro vs con?
Static threads
  Pool of threads created and are allocated work, but do not terminate until clean up
  Pro vs con?

## Slide 34: Summary
Overview of shared memory architectures
Interconnects
Memory hierarchy
Cache coherence
  Update vs. invalidate
  Snoopy vs. directory
Reading:
  Chpt2 of Kumar’s book