## Slide 1: “Distributed Address Space: Network Topologies”

## Slide 2: Outline
Overview of distributed address space
Performance Metrics
Topologies
Routing

## Slide 3: Distributed Address Space
Each processor has its own local address space
Processors share data via explicit message passing
CPU
CPU
MEM
MEM
CPU
CPU
MEM CPU
CPU MEM
MEM
MEM

## Slide 4: Distributed Address Space
Important aspects are:
  Interconnect
  Message routing mechanism
These aspects determine:
  Performance
  Scalability
  cost

## Slide 5: Interconnect Networks
Carry data between processors
Interconnect components
  Switches
  Links(wires, fiber)
Interconnect network flavors
  Static network: point-to-point comm links
    Direct networks
  Dynamic networks: switches and comm links
    Indirect network

## Slide 6: Static vs. Dynamic Networks
Static/direct network
Dynamic/indirect network

## Slide 7: Performance Metrics
Degree: number of links per node
Diameter: maximum distance between any two processors.
Connectivity: the multiplicity of paths between processors.
– Arc connectivity: the minimum number of links that need to be removed in order to bread the network into two disjoint parts
Bisection width: the minimum number of links that need to be removed in a network to separate the processor into two halves
Cost:
~ # links and switches

## Slide 8: Network Topologies: Bus
All processors access a common bus for exchanging data
Used in simples and earliest parallel machines
Advantages
– ?
Disadvantages
– ?

## Slide 9
Bus
Since much of the data accessed by processors is local to the processor, a local memory can improve the performance of bus-based machines

## Slide 10: Crossbar Network A crossbar network uses an p××××m grid of switches to connect p inputs to m outputs in a non-blocking manner

## Slide 11: Crossbar Network
Suppose a p×p crossbar, its cost = ?
Examples:
  Full crossbar
    Earth simulator: custom 640-way single-stage crossbar
  Crossbar as building block
    Rice RTC (retired in 2008): 16-way crossbar switches in 128- way Clos network

## Slide 12: Multistage Interconnect
Buses
  Excellent cost scalability
  Poor performance scalability
Crossbars
  Excellent performance scalability
  Poor cost scalability
Multistage interconnects
  Compromise between these extremes

## Slide 13: Multistage Network
Schematic of a typical multistage interconnection network (processor-to-memory, e.g., BBN Monarch)

## Slide 14: Multistage Omega Network
One of the most commonly used multistage interconnects
Organization
  log p stages
  p number of inputs/outputs
At each stage, input i is connected to output j if:
If p=2k, then j=?

## Slide 15: Omega Network Stage

## Slide 16: Omega Network Switches
The perfect shuffle patterns are connected using 2×2 switches
The switches operate in two modes:
– Cross-over vs. pass-through.
(a) pass-through
0 |  | 0 | 0 | 0
1 |  | 1 | 1 | 1
(b) cross-over

## Slide 17: Multistage Omega Network
A complete omega network connecting eight inputs and eight outputs.
Cost: ??

## Slide 18: Omega Network Routing
Let
  s= binary representation of the source processor
  d= binary representation of the destination processor or memory
The data traverses the link to the first switching node
if the most significant bit of s and d are the same pass-through
else
cross-over
Strip off leftmost bit of s and d
Repeat for each of the log(p) switching stages

## Slide 19: Omega Network Routing
An example of blocking in omega network: one of the messages (010 to 111 or 110 to 100) is blocked at link AB

## Slide 20: Star & Complete Connected Network
Star
  Static counterpart of bus
  Every node connected only to a common node at the center
  Distance between any pair of nodes is O(1)
Complete connected network
  Static counterpart of crossbar
  Each processor is connected to every other processor.
  The number of links in the network scales as O(p2)

## Slide 21: Linear Array
Each node has two neighbors: left & right
If connection between nodes at ends: 1D torus (ring)
  Diameter of a ring is ?
  Arc connectivity of a ring is ?
  Bisection width of a ring is ?

## Slide 22: Multidimensional Meshes
Mesh: generalization of linear array to 2D or 3D
Mesh with wrap around: torus
K-dimensional mesh
– Node has 2k neighbors

## Slide 23: Multidimensional Meshes
Diameter of a 2D mesh is
? ; for torus it is ?
Arc connectivity of a 2D mesh is ?; for torus it is ?
Bisection width of a 2D mesh is
? ; for torus it is ?

## Slide 24: Hypercube
A hypercube is a multidimensional mesh with exactly two processors in each dimension
In a d-dimensional hypercube, each processor is connected with d other processors

## Slide 25: Hypercube

## Slide 26: Hypercube
Hypercubes can be constructed recursively
Two processors are connected if ?
Consider two processors with labels s and t, what is the Hamming distance for the two processors?

## Slide 27: Hypercube
Diameter of a hypercube is ?
Arc connectivity of a hypercube is ?
Bisection width of a hypercube is ?

## Slide 28: Trees
Processing nodes
Switching nodes
(a) Static tree network
(b) dynamic tree network
(a)
(b)

## Slide 29: Tree Properties
Distance between any two nodes is no more than 2logp
Problem:
  Links higher up the tree potentially carry more traffic than those at the lower levels
Solution: fat tree
  Using wider links at higher levels in the tree
Fat tree network for 16 processors

## Slide 30: Tree
Diameter of a tree is ?
Arc connectivity is ?
Bisection width is ?

## Slide 31: Metrics for Static Interconnects
Network
Diameter
Bisection Width
Arc Connectivity
Cost
(No. of links)
Completely-connected
Star
Complete binary tree
Linear array
2-D mesh, no wraparound
2-D wraparound mesh
Hypercube
Wraparound k-ary d-cube

## Slide 32: Metrics for Dynamic Interconnects
Network
Diameter
Bisection Width
Arc Connectivity
Cost
(No. of links)
Crossbar
Omega Network
Dynamic Tree

## Slide 33: Message Passing Costs
Startup time (ts)
  Time spent at sending and receiving nodes
  Including?
Per-hop time (th)
  A function of number of hops
  Including?
Per-word transfer time (tw)
  Including?

## Slide 34: Store-and-Forward Routing
Definition:
– Message traversing multiple hops is completely received at an intermediate hop before being forwarded to the next hop
The total communication cost for a message of size
m words to traverse l communication links is
Typically, th is small
Thus, approximate store-and-forward message cost

## Slide 35: Routing Techniques
P0 P1 P2 P3
time
time
(1) A single message sent over A store-and-forward network
P0 P1 P2 P3
P0 P1 P2 P3
time
(2) The same message broken into two parts and send over the network
(3) The same message broken into four parts and sent over the network

## Slide 36: Packet Routing
Store-and-forward makes poor use of comm resources
Packet routing
  Break messages into packets
  Pipeline them through the network
Packets may take different paths, thus each packet must carry
  Routing information
  Error checking
  Sequencing information
The total communication time for packet routing is
tw accounts for overheads in packet headers

## Slide 37: Cut-Through Routing
Packet routing in the extreme
  Divide messages into basic units called flits
  Flits are typically small -> header info must be small
What are the differences between cut-through and packet routing?
Used in today’s infiniband networks

## Slide 38: Cut-Through Routing
Communication time for cut-through routing is
This is identical to packet routing; however, tw is typically much smaller
Typically, th smaller than ts and tw
Approximate communication time using cut-through routing is

## Slide 39: Simplified Cost Model for Messages
Valid for only uncongested networks
If a link takes multiple messages
  corresponding tw term must be scaled up by # messages
Network congestion varies by
  Communication pattern
  Match between pattern and network topology
Communication models must account for congestion

## Slide 40: Routing Variants
Routing mechanism determines the path a message takes through the network when going from a source to a destination processor
Minimal or non-minimal routing
Deterministic or adaptive

## Slide 41: Routing Challenges
Routing must prevent deadlocks
  Use dimension-ordered or e-cube routing
Routing must avoid hot-spts
  Can use two-step routing
  Message from s to d: first sent to a randomly chosen intermediate processor i; then forward from i to destination d

## Slide 42: Example: E-cube Routing in Hypercube
If the message is at processor Pi and needs to go to Pd, compute s  Pi  Pd Send message along dimension k from Pi where k is the least significant non-zero bit in s
Continues this process at each successive processor until Pd is reached
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111

## Slide 43: Example: XY Routing in 2D Mesh
Message sent along X dimension until destination’s X coordinate is reached
Then message is sent along Y dimension until it reaches destination processor
Called dimension-order routing

## Slide 44: Summary
Overview of distributed address space
Performance Metrics
Topologies
Routing
Reading material: Kumar – Chpt 2