## Slide 1: How to Run Applications Fasters?
There are 3 ways to improve performance
  Work harder
  Work smarter
  Get help
Computer analogy
  Use faster hardware : e.g., reduce the time per instruction (clock cycle)
  Optimize algorithms and techniques, customized hardware
  Multiple computers to solve the problem = to increase no. of instructions executed per clock cycle

## Slide 2: Sequential Architecture Limitations
Sequential architectures reaching physical limitation
Hardware improvements like pipelining, superscalar, …., are not scalable and require sophisticated compiler technology
Vector processing works well for certain problems
=> Technology push!

## Slide 3: Technology Trends: Microprocessor Capacity
Moore’s Law
2X transistors/Chip Every 1.5 years
Called “Moore’s Law”
Microprocessors have become smaller, denser, and more powerful.
Gordon Moore (co-founder of Intel) predicted in 1965 that the transistors density of semiconductor chips would double roughly every 18 months.

## Slide 4: Microprocessor (1970-2000)
10000000
1000000
Transistors (Thousands)
100000
Frequency (MHz)
10000
0
1
10
100
1000
1970
1975
1980
1985
1990
1995
2000

## Slide 5: Hidden Parallelism Tapped Out
In the past: increasing circuit density to performance
Microprocessors - Superscalar designs were the state of the art :
  What is superscalar?
  Dynamic scheduling
  Speculative execution
  Non-blocking caches
Apparent path to higher performance?
  Wider instruction issue
  Support for more speculation
Unfortunately, these sources have been used up!

## Slide 6: Hidden Parallelism Tapped Out
Unfortunately, these sources have been used up!
Two factors:
  Fundamental circuit limitations
    delays ⇑ as issue queues ⇑ & multi-port register files ⇑
    Increasing delays limit performance returns from wider issue
  Limited amount of ILP
• ?
“The case for a single-chip multiprocessor”, K. Olukotun, B. Nayfeh,
L. Hammond, K. Wilson, and K. Chang, ASPLOS-VII, 1996.

## Slide 7: Performance Comparison
The 6-issue has higher IPC than 2-issue, but far less than 3x
Possible reasons??

## Slide 8: Impact of Device Shrinkage
What happens when the feature size (transistor size) shrinks by a factor of x ?
Clock rate goes up by x because wires are shorter
  actually less than x, because of power consumption
Transistors per unit area goes up by x2
Die size also tends to increase
  typically another factor of ~x
Raw computing power of the chip goes up by ~ x4 !
  typically x3 is devoted to on-chip
So most programs x3 times faster, without changing them

## Slide 9: Manufacturing Issues Limit Performance
Manufacturing costs and yield problems limit use of density
Moore’s 2nd law (Rock’s law): ??
Demo of 0.06
micron CMOS
Source: Forbes Magazine
Yield
-What percentage of the chips are usable?
-E.g., Cell processor (PS3) is sold with 7 out of 8 “on” to improve yield

## Slide 10: Power Density Limits
8086
100
1000
10000
Hot Plate
Reactor
Nozzle Nuclear
Sun’s Surface
Rocket
Source: Patrick Gelsinger, Shenkar Bokar, Intel
Scaling clock speed (business as usual) will not work
Concurrent systems are more power efficient
– Why??
4004
8008
8080
8085
286
386
486
Pentium®
P6
1
10
1970
1980
2000
2010
1990
Year
Power Density (W/cm2)
High performance serial processors waste power
  Speculation, dynamic dependence checking, etc. burn power
  Implicit parallelism discovery
More transistors, but not faster serial processors

## Slide 11: Revolution in Processors
10000
100000
1000000
10000000
Transistors (Thousands) Frequency (MHz)
Power (W) Cores
1000
100
10
1
0
1970 1975 1980 1985 1990 1995 2000
Chip density is continuing increase ~2x every 2 years
Clock speed is not
Number of processor cores may double instead
Power is under control, no longer growing
2005
2010

## Slide 12: Multicore Chips
Single core trends are gloomy
  Performance is difficult to exploit
  Perf/power deteriorate
Fill the die w/ cache has limited value
  Between 2MB and 4MB cache – gain is diminishing
Solution: more cores on a die
  Benefits: higher performance, constant perf/power, less complexity, lower wire delays
  Challenges: scalability of interconnect, scalability of application, limited memory BW, power
Other solutions: more integration - memory controller, special functions/accelerators, graphics, …

## Slide 13
Why powerful computers are
parallel
all
All major processor vendors are producing parallel computers, because ???

## Slide 14: Memory Bottleneck
Cores share finite off-chip bandwidth
Latency cannot be improved significantly
  It is already 100s of cycles
To hide latency, need more parallelism than number of cores, schedule data

## Slide 15: Memory is Not Keeping Pace
Source: David Turek, IBM
Technology trends against a constant or increasing memory per core
Memory density is doubling every three years; processor logic is every two
Storage costs ($/MB) are dropping gradually compared to logic costs
Cost of Computation vs. Memory
Question: Can we double concurrency without doubling memory?
Strong scaling: ?
Weak scaling: ?
CS546
Source: IBM

## Slide 16: More Limits:
How fast can a serial computer be?
r = 0.3 mm
1 Tflop/s, 1 Tbyte sequential machine
Consider the 1 Tflop/s sequential machine:
  Data must travel some distance, r, to get from memory to processor.
  To get 1 data element per cycle, this means 1012 times per second at the speed of light, c = 3x108 m/s. Thus r < c/1012 =
0.3 mm.
Now put 1 Tbyte of storage in a 0.3 mm x 0.3 mm area:
– Each bit occupies about 1 square Angstrom
No choice but parallelism

## Slide 17: The TOP500 Project
Listing the 500 most powerful computers in the world
Yardstick: Rmax of Linpack
  Solve Ax=b, dense problem, matrix is random
  Dominated by dense matrix-matrix multiply
Update twice a year:
  ISC’xy in June in Germany
  SCxy in November in the U.S.
All information available from the TOP500 web site at: www.top500.org

## Slide 18: Units of Measure in HPC
High Performance Computing (HPC) units are:
  Flop: floating point operation
  Flops/s: floating point operations per second
  Bytes: size of data (a double precision floating point number is 8)
Typical sizes are millions, billions, trillions…
Mega
Mflop/s = 106 flop/sec Mbyte = 220 = 1048576 ~ 106 bytes
Giga Tera Peta Exa Zetta Yotta
Gflop/s = 109 flop/sec Tflop/s = 1012 flop/sec Pflop/s = 1015 flop/sec Eflop/s = 1018 flop/sec Zflop/s = 1021 flop/sec Yflop/s = 1024 flop/sec
Gbyte = 230 ~ 109 bytes
Tbyte = 240 ~ 1012 bytes
Pbyte = 250 ~ 1015 bytes
Ebyte = 260 ~ 1018 bytes
Zbyte = 270 ~ 1021 bytes
Ybyte = 280 ~ 1024 bytes

## Slide 19: Performance Development
100 Tflop/s
10 Tflop/s
1 Pflop/s
100 Pflop/s
10 Pflop/s
2.57 PFlop/s
31.12 TFlop/s
43.66 PFlop/s
SUM
1 Gflop/s
1 Tflop/s
100 Mflop/s
100 Gflop/s
10 Gflop/s
59.7 GFlop/s
400 MFlop/s
1.17 TFlop/s
N=1
N=500

## Slide 20: Core Count

## Slide 21: Moore’s Law reinterpreted
Number of cores per chip will double every two years
Clock speed will not increase (possibly decrease)
Need to deal with systems with millions of concurrent threads
Need to deal with inter-chip parallelism as well as intra-chip parallelism

## Slide 22: Parallel Computers
Cores with pipelining and short vectors
Multicore processors
Shared memory multiprocessor nodes
Scalable parallel systems

## Slide 23: Typical Parallel Machine
Chip/Socket
Core
Core
Core
Core

## Slide 24
Node/Board
Chip/Socket
Chip/Socket
Chip/Socket
Core
Core
Core
Core
Core
GPU
GPU
GPU …

## Slide 25
Cabinet
Shared memory programming between processes on a board and
a combination of shared memory and distributed memory programming between nodes and cabinets
Node/Board
Node/Board
Node/Board
Chip/Socket
Chip/Socket
Chip/Socket
Core
Core
Core
Core
…
Core
…
GPU
GPU
GPU

## Slide 26
Cabinet
Cabinet Cabinet
…
Combination of shared memory and distributed memory programming
Switch
Node/Board
Node/Board
Node/Board
Chip/Socket
Chip/Socket
Chip/Socket
Core
Core
Core
Core
…
Core
…
GPU
GPU
GPU

## Slide 27: Exascale Systems w/ a cap of $200M and 20MW
Jack Dongarra SC’13

## Slide 28: Future Computer Systems
Most likely to be a hybrid design
  Think standard multicore chips and accelerators (GPUs)
Today accelerators are attached
Next generation will be more integrated
DOE CORAL (Collaboration of Oak Ridge, Argonne, and Livermore)
  Procurement of pre-exascale supercomputers
  Summit at ORNL and Sierra at LLNL: Nvidia GPU- accelerated systems based on the IBM OpenPOWER platforms
    NVLink is a key building block in these machines, which enables IBM POWER CPUs and Nvidia GPUs to access each other’s memory fast
  Aurora at ANL: Intel Xeon Phi Gen 3 with Cray “Shasta” platform

## Slide 29: Titan at ORNL: Cray XK7 with AMD Opteron and Nvidia Tesla

## Slide 32: Principles of Parallel Computing
Parallelism and Amdahl’s Law
Finding and exploiting granularity
Preserving data locality
Load balancing
Coordination and synchronization
Performance modeling
All of these things make parallel programming more difficult than sequential programming!

## Slide 33: Challenges of Parallelism
“Automatic” parallelism in modern machines
  Bit level parallelism – within floating point operations
  Instruction level parallelism (ILP) – multiple instructions per clock cycle
  Memory system parallelism – overlap of memory accesses with computation
  OS parallelism – multiple jobs run in parallel on SMPs
There are limitations to all of these!
To achieve high performance, the programmer needs to identify, schedule and coordinate parallel tasks and data!

## Slide 34: Challenges of Parallelism
Applications are often very sophisticated
  E.g., adaptive algorithms may require dynamic load balancing
Algorithm development is harder
  Complexity of specifying and coordinating concurrent activities
  Algorithmic scalability losses
  Serialization and load imbalance
Software development is much harder
  Lack of development tools and programming models
  Subtle program errors: race conditions
  Multilevel parallelism is difficult to manage
  Communication and/or IO bottlenecks
Rapid pace of change in computer system architecture
  A parallel algorithm for one machine may not be a good match for another
  Homogeneous multicore processors vs GPGPU
Extreme scale exacerbates inefficiencies

## Slide 35: Parallel Systems
All processors will be multi-core
All computers will be massively parallel
All programmers will be parallel programmers
All programs will be parallel programs
The key challenge: how to enable mainstream developers to scale their applications on machines!
  Algorithms – scalable, asynchronous, fault tolerant
  Programming models and systems
  Data management
  Runtime system support

## Slide 36: Enterprise Applications
Program = web search, email, map/GIS, …
Computer = 1000’s computers, storage, network
Warehouse-sized facilities and workloads
New datacenter ideas (2007-2008): truck container (Sun), floating (Google), datacenter-in-a-tent (Microsoft)
How to enable innovation in new services w/o first building and capitalizing a large company?

## Slide 38: Enterprise Datacenter
A 50-rack data center
  X 64 blades per rack
  X 2 sockets per blade
  X 32 cores per socket
  X 10 VMs per core
  X 10 Java objects per VM
20,480,000 managed objects!

## Slide 39: Enterprise Scalability - Problem
How do you scale up?
  Run jobs processing 100’s of terabytes of data
  Takes 11 days to read on 1 computer
Need lots of cheap computers
  Fixes speed problem (15 min on 1000 computers), but
  Reliability issue: large computers fail every day
Need common infrastructure
  Must be efficient and reliable

## Slide 40: Enterprise Scalability - Solution
Open source Apache Project
Hadoop Core includes
  Distributed file systems – distribute data
  MapReduce – distribute application
Written in Java
Runs on commodity HW, Linux, Mac OS/X, Windows, …
Hadoop Clusters:
~20,000 machines running Hadoop @Yahoo! Hundreds of thousands of jobs per month

## Slide 41: Distributed and Cloud Computing
Peer-to-peer systems
  Flexible network of client machines logically connected by an overlay network
Data/computational Grids
  Heterogeneous clusters interconnected by high-speed network links over selected resource sites
Key enabler:
    Network vs. computer performance
    Computer speed doubles every 18 mo. vs. network speed doubles every 9 mo.
Key characteristics:
    Sharing data
    Distributing computation
    Coordinating problem solving
    Accessing remove instrumentation

## Slide 42: Cloud Computing
Cloud computing is Internet-based computing, whereby shared resources, software and information are provided to computers and other devices on-demand like a public utility (Wikipedia)
A cloud is a computing capability that provides an abstraction between the computing resource and its underlying technical architecture, enabling convenient, on-demand network access to a shared pool of configurable computing resources that can be rapidly provisioned and released with minimal management effort or service provide interaction (NIST)
CS546
Deployment models:
Public cloud
Private cloud
Hybrid cloud

## Slide 43: The Cloud Evolution
Ack. Manish Parashar (Rutgers)

## Slide 44: Cloud Stack
A seductive abstraction – unlimited resources, always on and accessible !
Multiple entry points: SaaS, PaaS, IaaS, HaaS
Pay as you go, for what you use!
Economy - IT outsourcing, TCO, capital costs, operation costs, …

## Slide 46: Summary
What is parallel computing
Why parallel computing
  Application pull
  Technology push
Distributed and cloud computing
Reading:
  Kumar – ch 1; Foster – ch 1